## Slide 1
ADDING EXTERNAL SATA HARD DRIVES & SSDs TO A COMPUTER
WITHOUT USING AN USB TO M.2 SSD ADAPTER

## Slide 2: Web location for this presentation:
http://aztcs.apcug.org
Click on
"Meeting Notes"

## Slide 3: SUMMARY
By using low-cost SATA data cables and a separately-purchased SATA power supply, you can add internal (SATA) hard drives and 2.5-in. SSDs outside of your computer. Doing so lets you install SATA drives outside of your computer without incurring the expense and slowdown of using USB hard drive adapters or enclosures.

## Slide 4: CONFIGURATION
SATA hard drive or SATA 2.5-in. SSD outside of the computer connects to a SATA data cable which then connects to a SATA data slot on the motherboard of the computer.
The drive that is outside of the computer also is attached a SATA power supply. The drive that is outside of the computer is cooled by a fan that connects to a separate Molex power supply.

## Slide 5: SATA DATA CABLE(S)
https://www.amazon.com/StarTech-com-36in-SATA-Serial-Cable/dp/B0000AZK6R/
Note: a SATA data female connector will NOT work with at a SATA data port at the motherboard

## Slide 6: MALE-TO-MALE SATA DATA ADAPTERS
https://www.amazon.com/dp/B017QZQFS2?
These are needed if you need to connect two SATA data cables together to make a longer one.

## Slide 7: MOLEX POWER SUPPLY
https://www.amazon.com/Coolerguys-100-240v-Molex-Power-Adapter/dp/B000MGG6SC/
This power supply supplies power to BOTH the SATA power port of the SATA hard drive (or SATA 2.5-in. SSD) AND to the fan for the hard drive (if you are installing a hard drive)

## Slide 8: MOLEX SPLITTER
https://www.amazon.com/Computer-Molex-Power-Supply-Splitter/dp/B07945ZZ59/
The single power output of the Molex power supply must be shared with both the power port of the hard drive (or the 2.5-in. SSD) and the fan for the hard drive (if you are installing a hard drive)

## Slide 9: MOLEX TO SATA POWER CABLE
https://www.amazon.com/Cable-Matters-3-Pack-Molex-Power/dp/B00STNUB04/
This cable goes from the Molex splitter to the SATA power port of the hard drive or the SATA power port of the 2.5-in. SSD.

## Slide 10: FAN FOR THE HARD DRIVE
https://www.amazon.com/dp/B07FDW4BNX?