## Slide 1
2: Wi-Fi MESH

## Slide 2: Web location for this presentation:
2
http://aztcs.apcug.org
Click on "Meeting Notes"

## Slide 3: SUMMARY
3
To increase the range and signal strength of a Wi-Fi local network, router, you can use a "mesh" which consists of two or more routers working cooperatively together to provide a coordinated Wi-Fi system.

## Slide 4: TOPICS
Mesh Advantages

## Slide 5: MESH ADVANTAGES
A "mesh" is a named grouping of two or more connected Wi-Fi routers that work together to provide you with: a larger coverage area, self-healing recovery from router failures, and hand-offs when user equipment moves between the actual coverage of each individual router

## Slide 6
INTERNET PROVIDER'S GATEWAY BOX
STEEL STAIRWELL & METAL FURNITURE
MY OFFICE AREA NOW HAS Wi-Fi COVERAGE
(ASUS) (MESH) ROUTER #1
ASUS MESH ROUTER #2
COSTLIER NETGEAR EXTENDER
CHEAPER
Wi-Fi EXTENDER

## Slide 7
INTERNET PROVIDER'S GATEWAY BOX
STEEL STAIRWELL & METAL FURNITURE
ASUS MESH ROUTER #1 $220
(Can be part of a mesh)
ASUS MESH ROUTER #2
$220
(Part of a mesh)
COSTLIER NETGEAR EXTENDER
$100
CHEAPER
Wi-Fi EXTENDER
$60

## Slide 8
INTERNET PROVIDER'S GATEWAY BOX
STEEL STAIRWELL & METAL FURNITURE
(ASUS) (MESH) ROUTER #1 $220
(Can be part of a mesh)
ASUS MESH ROUTER #2
$220
(Part of a mesh)
COSTLIER NETGEAR EXTENDER
$100
CHEAPER
Wi-Fi EXTENDER
$60

## Slide 9: MESH ADVANTAGES (continued)
For the mesh option, I need to have a mesh-capable router at both the North end of the house and the South end of the house and both routers have to belong to the same "mesh" system which, in practice", means that both routers have to belong to the same mesh group of the same manufacturer:

## Slide 10
INTERNET PROVIDER'S GATEWAY BOX
STEEL STAIRWELL & METAL FURNITURE
MY OFFICE AREA NOW HAS Wi-Fi COVERAGE
ASUS MESH ROUTER #1
ASUS MESH ROUTER #2
COSTLIER NETGEAR EXTENDER
CHEAPER
Wi-Fi EXTENDER

## Slide 11: MESH ADVANTAGES (continued)
In our live example, the two "ASUS" routers are part of a mesh. However, the Netgear Wi-Fi extender is not part of the mesh, even if it broadcasts the same "mesh1" SSID as the two "ASUS" routers.

## Slide 12
ASUS MESH ROUTER #1
"mesh1" at 2.45 Ghz RF band
"mesh1" at 5 Ghz RF band
"mesh1" at 6 Ghz RF band
ASUS MESH ROUTER #2
"mesh1" at 2.45 Ghz
"mesh1" at 5 Ghz
"mesh1" at 6 Ghz
COSTLIER NETGEAR EXTENDER
"mesh1" at 2.45 Ghz
"mesh1" at 5 Ghz

## Slide 13: MESH ADVANTAGES (continued)
For the mesh option, I need to have a mesh-capable router at both the North end of the house and the South end of the house and both routers have to belong to the same "mesh" system which, in practice", means that both routers have to belong to the same mesh group of the same manufacturer:

## Slide 14: MESH ADVANTAGES (continued)
Mesh routers have more powerful transmitter-receivers and most have extra transmitter-receivers dedicated to backhaul communications: In my home, the two ASUS mesh routers let me use wireless Wi-Fi backhaul links to "punch through" the metal stairwell where none of the extenders that I have tried are able to do so !

## Slide 15: MESH ADVANTAGES (continued)
The following diagram shows the extra Wi-Fi transmitter-receivers that the two ASUS mesh routers use for backhaul communications and administration of the "AiMesh" mesh group. The "AiMesh" brand of mesh is proprietary to the ASUS company.

## Slide 16: MESH ADVANTAGES (continued)
These extra transmitter-receivers are not seen by my user equipment but you can see them using Wi-Fi analysis software apps:

## Slide 17
ASUS MESH ROUTER #1
[hidden SSID] for AiMesh at 2.45 Ghz [hidden SSID] for AiMesh at 5 Ghz
[hidden SSID] for AiMesh at 6 Ghz
ASUS MESH ROUTER #2
[hidden SSID] for AiMesh at 2.45 Ghz
[hidden SSID] for AiMesh at 5 Ghz
[hidden SSID] for AiMesh at 6 Ghz

## Slide 18
ASUS MESH ROUTER #1
[hidden SSID] for AiMesh at 2.45 Ghz [hidden SSID] for AiMesh at 5 Ghz
[hidden SSID] for AiMesh at 6 Ghz
ASUS MESH ROUTER #2
[hidden SSID] for AiMesh at 2.45 Ghz
[hidden SSID] for AiMesh at 5 Ghz
[hidden SSID] for AiMesh at 6 Ghz

## Slide 19: MESH ROUTERS HAVE ADVANTAGES OVER Wi-Fi EXTENDERS (continued)
This moderately-priced pair of Asus mesh routers is the best deal that we have been able to find. You will need two of them for an entry-level mesh configuration: https://www.amazon.com/dp/B0DHWCQ3FP (You have to have two of these to create a Wi-Fi mesh setup.)

## Slide 22: FOR GREATER AREA COVERAGE, YOU CAN USE THE NETGEAR'S VARIOUS MESH CONFIGURATIONS
https://www.amazon.com/stores/page/54AA6656-F644-4E52-B9CC-7F8ADDF0921B/?_encoding=UTF8&pd_rd_plhdr=t&pd_rd_i=B0D4JB6QJD

## Slide 23: FOR GREATER AREA COVERAGE, YOU CAN USE THE NETGEAR'S VARIOUS MESH CONFIGURATIONS (continued)
We do not recommend the lowest option that Netgear offers (the rightmost option) because it is unable to communicate at the most current Wi-Fi 7 (802.11be) level of Wi-Fi capability

## Slide 26: Wi-Fi MESH UNITS, AND Wi-Fi EXTENDERS (continued)
Wi-Fi mesh brands:
Amazon's "Eero 6"
Amazon's "TruMesh"
ASUS's "AiMesh"
ASUS's "ZenWiFi"
Google's "Nest Wifi"

## Slide 27: Wi-Fi MESH UNITS, AND Wi-Fi EXTENDERS (continued)
Wi-Fi mesh brands (continued):
Linksys' "Atlas"
Linksys' "Velop"
Netgear's "Orbi"
(TP-Link's "Deco")
(TP-Link's "EasyMesh")

## Slide 28: SECURITY CONCERNS FOR TP-LINK ROUTERS
https://nationalinterest.org/blog/techland/states-have-a-tp-link-problem
https://www.wired.com/story/tp-link-router-ban-investigation/

## Slide 29: SECURITY CONCERNS FOR TP-LINK ROUTERS (continued)
https://www.digitaltrends.com/computing/tp-link-router-alternatives/
https://www.slashgear.com/1855885/tp-link-router-ban-explained-is-it-safe-to-buy/

## Slide 30: SECURITY CONCERNS FOR TP-LINK ROUTERS (continued)
https://www.msn.com/en-us/news/technology/where-are-tp-link-routers-made-and-why-does-the-us-government-want-to-ban-them/ar-AA1HcCBY
https://www.micklerandassociates.com/blog/should-i-remove-tp-link-devices